## Slide 1: MAPA/MoDOT Quarterly Meeting
May 5th, 2026
Dan Smith, P.E.
Traffic Management & Operations Engineer

## Slide 2: PART 630—PRECONSTRUCTION PROCEDURES
Subpart J—Work Zone Safety and Mobility
This subpart establishes requirements and provides guidance for systematically addressing the safety and mobility impacts of work zones, and for developing strategies to help manage these impacts on Federal-aid highway projects.
Work zone assessment and management procedures. States shall develop and implement systematic procedures to assess likely work zone impacts to all highway workers and anticipated road users in project development and to manage safety and mobility impacts occurring during project implementation.
Work zone data. States shall use field observations, available work zone crash data, available safety surrogate data, available operational information, and available exposure data to monitor and manage work zone impacts for specific projects during implementation and to perform its work zone programmatic reviews.

## Slide 3: Subpart J—Work Zone Safety and Mobility
Training. States shall require that personnel involved in the development, design, implementation, operation, inspection, and enforcement of work-zone-related transportation management and traffic control be trained, appropriate to the job decisions each individual is required to make.
Work zone programmatic review. In order to assess the effectiveness of work zone safety and mobility processes and procedures, States shall perform a work zone programmatic review every 5 years and share that review with FHWA by the end of the 5-year review period.

## Slide 4: Subpart J—Work Zone Safety and Mobility
Significant projects. A significant project is one that, alone or in combination with other concurrent projects nearby, is anticipated to cause sustained work zone impacts (as defined in § 630.1004) that are greater than what is considered tolerable based on State policy and engineering judgment.
Transportation Management Plan. For significant projects (as described in § 630.1010), the State shall develop a TMP that consists of a TTC plan and addresses both TO and PIO components. For individual projects or classes of projects that the State determines to have less than significant work zone impacts, the TMP may consist only of a TTC plan. States are encouraged to consider TO and PIO issues for all projects.

## Slide 5: PART 630—PRECONSTRUCTION PROCEDURES
Subpart K—Temporary Traffic Control Devices
To decrease the likelihood of highway work zone fatalities and injuries to workers and road users by establishing minimum requirements and providing guidance for the use of positive protection devices between the work space and motorized traffic;
installation and maintenance of temporary traffic control devices; use of uniformed law enforcement officers during construction, utility, and maintenance operations;
and by requiring contract pay items to ensure the availability of funds for these provisions.
This subpart is applicable to all Federal-aid highway projects, and its application is encouraged on other highway projects as well.

## Slide 6
MUTCD Section 6M.02 Positive Protection and Temporary Traffic Barriers
Support:
Temporary traffic barriers, including portable or movable barriers, are devices designed to help prevent
penetration by vehicles while minimizing injuries to vehicle occupants, and to protect workers, bicyclists,
and pedestrians.
Guidance:
Except as otherwise required, at a minimum, longitudinal traffic barriers and/or other positive protection
devices should be considered in work zone situations that place workers at increased risk from motorized traffic,
and where positive protection devices offer the highest potential for improved safety for workers and road users.
Support:
Considerations for positive protection include, but are not limited to, the following circumstances:
A. Work zones that provide workers no means of escape from motorized traffic such as tunnels or bridges;
B. Long-term stationary work zones of two weeks or more resulting in substantial worker exposure to
motorized traffic;
C. Projects with anticipated operating speeds of 45 mph or greater, especially when combined with high
traffic volumes;
D. Work operations that place workers, pedestrians, or bicyclists close to travel lanes open to traffic; and
E. Roadside hazards, such as drop-offs or unfinished bridge decks, that will remain in place overnight
or longer.

## Slide 7: Subpart K—Temporary Traffic Control Devices
Positive protection devices. At a minimum, agencies shall use positive protection devices in work zones with high anticipated operating speeds that provide workers no means of escape from motorized traffic intruding into the workspace unless an engineering study determines otherwise. Positive protection devices shall be considered in other situations that place workers at increased risk from motorized traffic, and where positive protection devices offer the highest potential for increased safety for workers and road users such as:
  (1) Work zones that provide workers no means of escape from motorized traffic (e.g., tunnels, bridges, etc.);
  (2) Long-duration work zones (e.g., two weeks or more) resulting in substantial worker exposure to motorized traffic;
  (3) Projects with high anticipated operating speeds (e.g., 45 mph or greater), especially when combined with high traffic volumes;
  (4) Work operations that place workers close (e.g., within one lane width) to travel lanes open to traffic; and
  (5) Roadside hazards, such as drop-offs or unfinished bridge decks, that will remain in place overnight or longer.

## Slide 8: Subpart K—Temporary Traffic Control Devices
616.13.2 Positive Protection and Temporary Traffic Barriers (MUTCD Section 6M.02)
Subpart K
Positive protection devices. At a minimum, agencies shall use positive protection devices in work zones with high anticipated operating speeds that provide workers no means of escape from motorized traffic intruding into the workspace unless an engineering study determines otherwise. Positive protection devices shall be considered in other situations that place workers at increased risk from motorized traffic, and where positive protection devices offer the highest potential for increased safety for workers and road users such as: (MoDOT meets the above guidance. Since the original WZ Safety and Mobility register, MoDOT should review all the PPD guidance in EPG 616 and 617.)
Work zones that provide workers no means of escape from motorized traffic (e.g., tunnels, bridges, etc.);
Long-duration work zones (e.g., two weeks or more) resulting in substantial worker exposure to motorized traffic;
Projects with high anticipated operating speeds (e.g., 45 mph or greater), especially when combined with high traffic volumes;
Work operations that place workers close (e.g., within one lane width) to travel lanes open to traffic; and (MoDOT provide PPD for edge drop off but not for “within one lane width” for workers.)
Roadside hazards, such as drop-offs or unfinished bridge decks, that will remain in place overnight or longer.

## Slide 9: Subpart K—Temporary Traffic Control Devices
Project scope and duration;
Anticipated operating conditions including traffic volume, vehicle mix, and speeds through the work zone;
Anticipated traffic safety impacts;
Type of work (as related to worker exposure and crash risks);
Distance between traffic and workers, and extent of worker exposure;
Escape paths available for workers to avoid a vehicle intrusion into the work space;
Time of day (e.g., night work);
Work area restrictions (including impact on worker exposure);
Consequences from/to road users resulting from roadway departure;
Potential hazard to workers and road users presented by device itself and during device placement and removal;
Geometrics that may increase crash risks (e.g., poor sight distance, sharp curves);
Access to/from work space;
Roadway classification; and
Impacts on project cost and duration.

## Slide 10: Subpart K—Temporary Traffic Control Devices
Other traffic control measures:
Effective, credible signing;
Changeable message signs;
Arrow panels;
Warning flags and lights on signs;
Longitudinal and lateral buffer space;
Trained flaggers and spotters;
Enhanced flagger station setups or use of automated flagger assistance devices (AFADs);
Intrusion alarms;
Rumble strips;
Pace or pilot vehicle;
High-quality work zone pavement markings and removal of misleading markings;
Channelizing device spacing reduction;
Longitudinal channelizing barricades;
Work zone speed management (including changes to the regulatory speed or variable speed limits);
Law enforcement;
Speed Safety Cameras (where permitted by State/local laws;
Drone radar;
Worker and work vehicle/equipment visibility;
Worker training;
Public information and traveler information; Temporary traffic signals.
Protection or shadow vehicles used to protect workers and equipment from impacts by errant vehicles; and
Intelligent Transportation Systems (ITS) and other advanced technology solutions and strategies.

## Slide 11: Subpart J—Work Zone Safety and Mobility Subpart K—Temporary Traffic Control Devices
eCFR :: 23 CFR Part 630 Subpart J -- Work Zone Safety and Mobility
https://www.ecfr.gov/current/title-23/chapter-I/subchapter-G/part-630/subpart-J
eCFR :: 23 CFR Part 630 Subpart K -- Temporary Traffic Control Devices
https://www.ecfr.gov/current/title-23/chapter-I/subchapter-G/part-630/subpart-K

## Slide 12: Questions?
Daniel Smith
Traffic Management & Operations Engineer
(573) 526-4329
Daniel.Smith@modot.mo.gov
Notes: Add link page or section